DHANALAKSHMI COLLEGE OF ENGINEERING

Dr. V.P.R. Nagar, Manimangalam,

Chennai 601 301.

GE6152 - ENGINEERING GRAPHICS

(common for I year A & B section)

Assignment - 1

Unit-II

Projections of Points

- State the projection of points representing their quadrants and positions. All dimensions are in mm.

- Draw the projections of the following points on a common reference line. Take 30mm distance between the projections.

- A, 35mm above HP and 25mm in front of VP

- B, 40mm below HP and 15mm behind VP.

- C, 50mm above HP and 25mm behind VP

- D, 45 below HP and 25mm behind VP

- E, 30mm behind VP and on HP

Projections of Straight Lines

- A line AB has its end A 20mm above HP and 25mm in front of VP. The other end B is 45mm above HP and 55mm in front of VP.  The distance between the end projectors is 60mm. Draw its projections. Also find the true length and true inclinations of the line with HP and VP.

- A line AB 85mm long has its end A 60mm above HP and 65mm in front of VP. The end B is 25mm above HP and 20mm in front of the VP. Draw the projections and find its inclinations with HP and VP.

- The top view of a line is 65mm long and is inclined at 30º to the reference line. One end is 20mm above HP and 10mm infront of VP. The other end is 60mm above HP and is infront of VP. Draw the projections and find the true length of the line and its inclinations to HP and VP.

- The distance between the projectors of two points A and B is 70mm. Point A is 10mm above HP and 15mm infront of VP. Point B is 50mm above HP and 40mm infront of VP. Find the shortest distance between A and B, by rotating line method. Measure the true inclinations of the AB with VP and HP.

- A straight line AB has its end A 20mm above HP and 25mm in front of VP. The other end B is 60mm above HP and 65mm in front of VP. The ends of the line are on the same projectors. Draw its projections. Find the true length, true inclinations of the line with HP and VP.

- The end ‘P’ of a PQ, 70mm long is 15mm above the HP and 20mm in front of the VP. Q is 40mm above the HP. Its plan is inclined at 45° to the VP. Draw the projections of the line and find its true inclinations with VP and HP.

- A line PQ has its end P in HP and 40 mm in front of VP. Its front view is inclined is inclined at 50˚ to XY and has a length of 70 mm. The other end B is in VP. Draw its projections.

- A line AB 85 mm long has its end A 25 mm away from both reference planes and is in first quadrant of the line inclined at 500 to HP and 300 to VP. Draw its projections. Find its view lengths & apparent inclinations

- A line AB 100mm long has its front view inclined at an angle of 450 to the reference line separating the views. The end A is in VP and 25 mm above HP. The length of the front view is 60 mm. Draw the top view of the line and find the true inclinations of the line with the HP and VP.

- The mid point of a line AB 80mm long is 30mm above HP and 45mm infront of VP. It is inclined at 35º to HP and 55º to VP. Draw the projections.

- A line AB has its end A is in HP and 40mm in front of VP. Its front view is inclined at 50º to XY and has a length of 70mm. The other end B is in VP. Draw its projections.

- A Straight line ST has its end S, 10 mm infront of the VP and nearer to it. The midpoint m of the line is 50 mm infront of VP and 40 mm above HP. The front and top views measure 100 mm and 120 mm respectively. Draw the projections of the line. Also find its true length and true inclinations with the HP and VP.

Projections of Planes

- A pentagonal lamina of side 30mm is resting on HP with one of its

corner. The surface is at 60˚ to HP. The edge opposite to this corner is parallel to VP and further nearer to it. Draw its projections.

- A rectangular 70 X 40 mm one of its shorter edges in the HP, inclined at 40o to VP. Draw its front view if its top view is a square of side 40 mm.

- A circular plate of 50 mm diameter, appears as an ellipse in the front view, having its major axis 50mm long and minor axis 30 mm long. Draw the top view, when the major axis of the ellipse is horizontal.

- A hexagonal plate of side 30mm has one of its corners on HP and the opposite corner on VP. The plate makes an angle of 60º with HP and 30º with VP. Draw the projections of the plate.

- A circular lamina of diameter 70mm has the end A of the diameter AC on HP and the end C on VP. Draw its projections when its surface is inclined at 50º to HP and 40º to VP.

- A thin square plate EFGH of 40 mm side is having its corner G on HP. Diagonal EG is inclined at 40º to HP and diagonal FH inclined at 40º to VP and parallel to HP. Draw its projections by change of position method.

ISSUE DATE: 1.9.16 & SUBMISSION DATE: 12.9.16

Prepared by

R. SENDIL KUMAR, P.V. ELUMALAI

Assistant Professor/Mechanical

Dhanalakshmi College of Engineering,

Dr. V.P.R. Nagar, Manimangalam, Chennai 601 301.